## Slide 1: San Joaquin Valley VisionEval Training
December 19, 2025
1

## Slide 2: Introductions
RSG and MPO Staff
Format for the session
  Presentation with informal Q&A throughout
  Set aside Q&A time
  Breaks
  Screen sharing for demos
Presented by: Nick Fisher

## Slide 3: Training Overview
Part 1 (8:00am-10:45am)
Introduction
  What is VisionEval?
  Documentation & Resources
VisionEval Basics
  Overall workflow
  Geography structure
  Inputs
  Packages & Modules
  VisionEval Model Framework
Break (10:45am – 11:00am)
Part 2 (11:00am – 12:30pm)
Overview of provided models
Model folder structure
How to run a base model
How to test a future scenario
Lunch Break (12:30am – 1:00pm)
Part 3 (1:00pm – 3:00pm)
Querying outputs
How to run multiple future scenarios
Input/output visualizer guide
Presented by: Nick Fisher
Notes: Part 1:
Slides 1 – 60
165 min: 2.75 min per slide avg.

## Slide 4: Getting Setup
Confirm Version of R available on your machine = 4.3.3.
Download and confirm Rstudio is available
Ideally, although not necessary today, is to have Rtools 4.3 installed
Install the pre-built version of VisionEval for SJV
Presented by: Nick Fisher

## Slide 5: Part 1
8:00 am – 10:45 am
1. Introduction to VisionEval
2. VisionEval Basics
5
Presented by: Jon Slason

## Slide 6: 1. Introduction to VisionEval
1.1 What is VisionEval?
1.2 Documentation & Resources
Presented by: Jon Slason
Notes: Jon

## Slide 7: What is VisionEval?
An econometric travel demand model that uses disaggregate demand and an aggregate supply to forecast travel behavior for households within its model region
A tool used for scenario planning
Estimated on readily available data including National data such as the National Household Travel Survey (NHTS) then calibrated to local conditions (PUMS, HPMS, travel surveys, travel models).
Econometric framework for monetized costs (time & out of pocket) via a household travel budget. (e.g., congestion charges, fuel taxes, electrification effects)
Sensitive to land use, operational tactics, and policy tactics (e.g., TDM, induced travel, signal coordination, teleworking).
Runs quickly (run hundreds of scenarios in a short timeframe) because it lacks a specific network to assign trips. It is a daily travel model rather than a trip model.
Results can be viewed in an interactive visualizer and are available in output files (CSVs, SQL, Excel, etc.).
Open Source. Runs in R Studio
Presented by: Jon Slason

## Slide 8: Answering the Important Questions First How Does VisionEval Fit in the Process?
Presented by: Jon Slason
Notes: Originally developed in Oregon when they were struggling to better understand the travel behavior / land use nexus – combined with questions around energy, GHG, and uncertainty around pricing, demographics, etc.

## Slide 9: Connecting to Performance Measures How is VisionEval Used?
Used to Support:
Long-Range Planning Initiatives
Land-Use and Zoning Analyses
Climate Action, Resiliency, & EV Plans
Scenario Planning
Strategic investment & policy priorities
VMT targets
Zoning changes
Comprehensive plan priorities
Density, diversity of uses
Vehicle choice and availability
GHG targets and reduction pathways
Fuel tax revenues
Energy and fuel consumption
Community trade-off decisions Long-term investments
To Understand Impacts On…
Presented by: Jon Slason

## Slide 10: Open Source Tools Need Support
Members of the now disbanded Pooled Fund managed by FHWA are reorganized and will be pursuing a VisionEval pooled fund managed by Virgina DOT.
The tasks are primarily around the maintenance of the tool, updates to packages and sub-modules, external data, code development, extensions and enhancements, and supporting agencies apply the tool.
Contact Tara Weidner at Oregon DOT at
tara.j.weidner@odot.oregon.gov
If you would like to learn more about how to be involved in the Pooled Fund effort.
Presented by: Jon Slason

## Slide 11: Quantitative Exploratory modeling
VisionEval can run hundreds (& thousands) of possible future options. Using exported data (SQL databases and CSVs) we can 'goal seek’ for desired performance results and identify the types of investment and policy inputs which produced desirable outcomes.
Individual runs can be analyzed.
Visualizers and other tools can help cut through the noise to identify relationships between specific inputs and outputs.
Identify particular policy objective(s) i.e., lowest VMT per capita and high transit use
Define the conditions i.e., high population growth, greater urban intensity, and high consumer adoption of shared AVs
Set the constraints i.e., acceptable level of user revenues & minimize travel cost burden on lower income households
Identify the best mix of investments and policies
Presented by: Jon Slason

## Slide 12: Documentation and Resources
The home for VisionEval documentation
Website for VisionEval documentation: https://visioneval.org/docs/
However, this site is also managed by FHWA and Volpe. Local cloned repo’s can be managed to push changes that will be reviewed by Volpe staff.
  https://github.com/VisionEval/VisionEval-Docs
Presented by: Jon Slason
Notes: Jump to a live demo of the documentation. This would be helpful for show the users the type and amount of information.

## Slide 13: Relevant Repos & VisionEval Versions
FHWA GitHub site for VisonEval: https://github.com/VisionEval/VisionEval-Dev
RSG uses the RSG fork of the –Dev repo for the SJV installation.
  https://github.com/RSGInc/VisionEval-Dev
The SJV VisionEval uses VE 3.1.2
Note: VE 4.0 is now available but was not used for this implementation. VE 4.0 beta became available more than halfway through the project. The models used here should be able to be run with the latest framework. The key changes involve installation and installation of custom packages.
The VE versions should be compatible for running models. Key differences include some functions for exporting results, queries, building the R environment, and installing packages.
Presented by: Jon Slason

## Slide 14: Relevant Repos & VisionEval Versions
The SJV VisionEval lives in the SJV-VE-Extras repo: https://github.com/RSGInc/SJV-VE-Extras
FresnoCOG will be given access to the repo to then share as appropriate with other agencies.
Presented by: Jon Slason

## Slide 15: 2. VisionEval Basics
2.1 Overall workflow
2.2 Geography Structure
2.3 Inputs
2.4 Packages and modules
2.5 VisionEval Model Framework
Presented by: Jon Slason
15

## Slide 16: 2.1 Overall “Big Picture” Workflow
Step 1: Install the VisionEval model
Step 2: Develop a Base Model for the region. The Base Model:
Defines the model geography (select zone structure and region boundary)
Defines the base and scenario years (e.g., 2020 and 2046)
Contains local input files calibrated to Base Scenario conditions in the region (including both observed base year data and estimates of future year conditions with no scenario policies applied.)
Estimates household and population data
Creates the reference Base Scenario and Future Scenario
Step 3: Develop Future Scenarios by adjusting specific input files for future years.
Update all the Step 2 inputs.
Future Scenarios are specific model runs. Possibilities exist for running hundreds of scenarios by creating unique inputs and running models are each unique combination of inputs.
Step 4: Run the models and extract and visualize results
Presented by: Jon Slason

## Slide 17: 2.2 VE Geography Structure
Presented by: Nick Fisher
17
Notes: Edna

## Slide 18: SJV Geography Structure
The SJV VisionEval uses the following geographies which are perfectly nested within each other:
Region: The entire model area (8 MPOs + 17 bordering counties)
Mareas: Metropolitan areas within the model SJV, defined by the MPO boundaries
Azones: Larger geographic areas such as cities or tracts. SJV uses a combination of urbanized areas and 2020 Census Tracts.
Bzones: Subdivision of Azones that represent individual neighborhoods. SJV uses 2020 Census Block Groups
Additional categorical levels:
  Location type (urban/town/rural)
SJCOG Marea VE geography structure
Presented by: Nick Fisher

## Slide 19
Interactive Session: showing the SJV model geographies
Presented by: Nick Fisher

## Slide 20: External Zones
SJV VisionEval includes 17 external zones to represent all 17 bordering counties
External zones are included to capture commuter travel into/out of the model region
External zone inputs need to be provided to run the model
Households and jobs in the external zones are designed only to include sufficient numbers to capture travel effects for those who travel to jobs in SJV or those who travel outside the Valley.
These are estimated using an analysis of LEHD data.
SJV VE’s geography includes external zones
Presented by: Nick Fisher

## Slide 21: 2.3 Inputs
Presented by: Nick Fisher
Notes: Nick

## Slide 22: Inputs
There are 65 inputs including ~300 input parameters, and can be classified into these general categories:
  Setup files: Required as basic parameters for VisionEval. These values do not change.
  Demographics inputs: Population and job demographics and composition for the model region.
  Land use inputs: Housing and developable land inputs to inform potential transit demand growth.
  System operations/ITS inputs: Inputs that define the level of system efficiencies and ITS technology deployment
  Transportation options inputs: Policy inputs that impact transportation option available to households
  Vehicles and fuels inputs: Inputs that later the vehicle fleet and fuel mix available
  Pricing inputs: Inputs that create additional costs for system users such as congestion charges, parking costs, or vehicle fees/taxes
azone_fuel_power_cost.csv
Input File | Description
bzone_dwelling_units.csv | Number of Dwelling Units by type (SF, MF, GQ) by Year by Bzone
azone_hhsize_targets.csv | Average household size & share of 1-person households by year by Azone
marea_congestion_charges.csv | Congestion Charges ($/mile) coverage of daily VMT by road type (Fwy, Arterial) by 5 congestion levels by year by Marea
region_hvytrk_powertrain_prop.csv | HD Truck powertrain (ICE, HEV, EV) shares by stock year
Examples of Input Files
Presented by: Nick Fisher
Notes: Nick

## Slide 23: Types of Inputs
All inputs are defined at a geography level. The name of the input file indicates the geography level of the input data. (e.g., azone_hh_pop_by_age, marea_lane_miles).
The majority of input files are CSV and each input file will have:
  Year field when inputs vary by model year
  Geo field when inputs vary by geography
  Field names identifying dataset names
Inputs are provided for:
  Base model (Inputs included in the out-of-the-box VisionEval model)
  SJV model (Inputs customized for the SJV model)
Inputs must be provided for SJV counties AND external zones
azone_fuel_power_cost.csv
Presented by: Nick Fisher
Notes: Nick

## Slide 24: Input Sources & Methodologies
For more details on model inputs, refer to the User Guide chapter on Model Inputs (https://visioneval.org/docs/model-inputs.html) or search the source code for specification data for a given input
Common sources for inputs include:
  MPO travel demand model network
  HPMS
  EPA SmartLocationDatabase
  US Census
  EPA
  GTFS feeds
  Caltrans
  CARB
  National Transit Database
  California DMV
  Federal, state, and county regulation websites
The full list of inputs with their description and sources will be provided in the model documentation
Input File | Methodology
bzone_dwelling_units.csv | Travel model data was used to calculate total dwelling units by type. Travel model data was used as a distribution of households by type for and official household forecast numbers were applied to the distribution
azone_hhsize_targets.csv | Used synthetic household and population data provided to determine the average household size and the number of single-person households.
marea_congestion_charges.csv | No congestion charges were assigned to the San Joaquin Valley Mareas.
region_hvytrk_powertrain_prop.csv | This input was developed using California vehicle registration data, and matches the heavy truck powertrain goals set in CARB’s Advanced Clean Trucks and Advanced Clean Fleets goals
Methodology examples
Presented by: Nick Fisher
Notes: Nick

## Slide 25: Example input: marea_transit_service.csv
Definition: The file contains the annual revenue-miles for different transportation modes in the Marea, including demand response, van-pool, rapid bus/BRT, commuter rail, monorail, streetcar, and heavy and light rail.
Methodology: Revenue miles were calculated from the National Transit Database for 2024, accounting for all service providers within each respective MPO region. No changes were assumed for 2046.
Presented by: Nick Fisher
Notes: Nick

## Slide 26: 2.4 Packages & Modules
Presented by: Jon Slason

## Slide 27: Elements Considered in the Strategic Model
Presented by: Jon Slason
Source: ODOT (adapted by RSG)

## Slide 28
Travel Demand
Household Composition
Built Form Factors (“D’s”)
Vehicles & Drivers & Fuels
Inputs - Policies
Fundamental Design of the Econometric Demand Model
Presented by: Jon Slason
Notes: Future Scenario Development: a handful of specific inputs to test. – toll pricing, a specific amount of transit or roadway miles, a land use scenario
Future Scenario Development: Identifying a range of investments and policies. Using low and high, or several specific input values. 75% to 150% of transit service, 50%-150% of parking costs, 75%-150% of pricing…
Strategic Modeling that explores hundreds and thousands of scenarios
Identify the scenarios which produced desirable results which support the Vision & Goals. Identify the inputs which lead to desired outcomes.

## Slide 29: Packages and Modules
VisionEval is built from packages, each containing specific modules
VisionEval works by running a sequence of modules (steps) which are defined in the run_model.R script
The default VisionEval model comes with the following base packages which are run roughly in the order shown 
Information on these packages can be found at: https://visioneval.github.io/docs/ve-estimation.html#ve-estimation
Module
Package
Module
Package
Presented by: Jon Slason

## Slide 30: SJV VE Packages
The SJV VE model uses a mix of default and custom packages
Custom packages are VE default packages that have been re-estimated using local data and updated to reflect the model region
The following packages are used in SJV VE:
Package | Description
VEPopulationSimSJV (custom) | Uses PopulationSim to create synthetic population
VESimHouseholdsSJV (custom) | Uses VE’s household synthesizer
VELandUseSVJ (custom) | Assigns employment, households, and land use types
VEPowertrainsAndFuelsSJV (custom) | Calculates energy consumption and emissions from transportation
VETransportSupply (default) | Calculates per capita roadway and transit supply
VETravelDemandWFH (default) | Includes the Multimodal Module estimated with 2017 NHTS data
VEHouseholdVehiclesDL, VELandUseDL and VETravelPerfromanceDL | Packages that reflect driverless and car service modules.
Presented by: Jon Slason

## Slide 31: Custom Package: VESimHouseholdsSJV
Contains modules to simulate households and their characteristics within model Azones. Household synthesis is estimated using 2020 PUMS data.
Modules include:
  CreateHouseholds: creates a Household table in the datastore and populates the table with datasets characterizing simulated households. Estimates model parameters.
  PredictWorkers: assigns workers by age to households and to noninstitutional group quarters population. It is a simple model which predicts workers as a function of the age composition of household members. Estimates model parameters.
  AssignLifeCycle: assigns a life cycle category to each household. The life cycle categories are similar, but not the same as, those established for the NHTS. Does not estimate model parameters.
  PredictIncome: predicts the income for each simulated household given the number of workers in each age group and the average per capita income for the Azone where the household resides. Estimates model parameters.
Presented by: Jon Slason

## Slide 32: Custom Package: VEPopulationSim
Household synthesis is done using PopulationSim and is an alternative to VESimHouseholds.
PopulationSim is an open-source platform that generates synthetic populations from PUMS data and user-defined control variables.
Control totals are flexible and can be applied at various geographic levels, e.g. household size, number of workers in household, income ranges, and age distribution bins.
PopulationSim documentation: https://activitysim.github.io/populationsim/
The main differences between the PopulationSim and VESimHousehold are:
  PopulationSim uses iterative fitting (IPF/IPU) to reweight Census PUMS microdata, ensuring household and person characteristics explicitly match local demographic control totals (by geography, age, income, etc.), producing outputs that are highly sensitive to data quality and geographic inputs.
  VESimHouseholds generates households using fixed probability tables and regression models estimated once from Census PUMS, assigning life cycle, household type, workers, and income without any iterative fitting or matching to control totals.
Bzone-level control totals are used as input to PopulationSim, and the synthetic households and persons it generates are used in the VEPopulationSim model
Presented by: Jon Slason

## Slide 33: Custom Packages: VELandUseSJV
New package being used in the SJV VE model. Based on research on land use conducted by Portland State by Professor Liming Wang and the creator VisionEval Brian Gregor.
This package assigns employment, households, and land use types across the model region.
The package has two implementations:
  Where land use type controls are provided:
    New implementation approach
    Uses simpler, more aggregate dwelling and employment targets which are then allocated to Bzones
    Dwelling unit and employment targets are described in terms of land use types.
  Where Bzone controls are provided:
    Default VE method.
    Uses asserted targets based on number of single- and multi-family dwelling units and number of jobs in each Bzone
    Households are allocated to housing types and Bzones based on their characteristics, e.g. income
Presented by: Jon Slason

## Slide 34: Custom Packages: VELandUseSJV
Population
Household synthesized by Azone based on forecasts of People by Age Group
Employment
Predict workers by Bzone based on forecasts of Total Employment, Retail Employment and Service Employment
Connect workers to households
Dwelling Units
Allocation households to Single Family, Multi Family and Group Quarters Dwelling Units By Bzone
Bzone Controls
Land Use Types
Set employment and dwelling type controls by land use types: area type (fringe, outer, inner, center), diversity type (residential, mixed, or employment), and location type (urban, rural)
Population
Household synthesized by Azone based on forecasts of People by Age Group
Employment
Predict workers by Bzone based on forecasts of Total Employment, Retail Employment and Service Employment and Land use type controls and transportation accessibility
Connect workers to households
Dwelling Units
Allocation households to Single Family, Multi Family and Group Quarters Dwelling Units By Bzone based on land use type controls and transportation accessibility
Land Use Type
Controls
Presented by: Jon Slason

## Slide 35: Custom Package: VEPowertrainsAndFuelsSJV
This package calculates energy consumption and emissions from transportation.
It adjusts the proportion of household vehicle sales by powertrain (internal combustion, hybrid, battery electric, and plug-in hybrids) and fuel type (gasoline, diesel, and CNG) for household vehicles, commercial vehicles, car service or ride-hailing, and heavy trucks.
It includes modules for inputting energy consumption characteristics of different vehicle technologies, carbon intensities of different fuels, functions for calculating energy consumption and emissions from household, commercial and public travel.
This package was customized for SJV VE using California DMV vehicle registration data and CARB zero-emission sales goals for 2046.
Chart: Household Autos
Presented by: Jon Slason
Year 2046 | Total Veh | BEV Vehicles | Share (%)
MCTC | 144162 | 95567 | 66.29
KCAG | 128225 | 76444 | 59.62
StanCOG | 493717 | 288036 | 58.34
MCAG | 283326 | 157783 | 55.69
KCOG | 856408 | 476249 | 55.61
TCAG | 410326 | 226206 | 55.13
FCOG | 913668 | 473034 | 51.77
SJCOG | 836360 | 374387 | 44.76
Year 2022 | Total Veh | BEV Vehicles | Share (%)
KCAG | 104153 | 849 | 0.82
MCTC | 125986 | 1001 | 0.79
StanCOG | 449514 | 3247 | 0.72
TCAG | 376771 | 2479 | 0.66
KCOG | 694250 | 4590 | 0.66
MCAG | 229261 | 1490 | 0.65
FCOG | 830439 | 5235 | 0.63
SJCOG | 633092 | 3663 | 0.58

## Slide 36: 2.5 VisionEval Model Framework
Presented by: Jon Slason
36

## Slide 37: Model Steps
The VisionEval framework is composed of eight core modeling steps. Each of which has sub-activities and models.
Each step includes a set of calculations and models estimated using data from the National Household Travel Survey (NHTS) and the US Census that operate on the input data as well as the results of the previous calculation step.
Presented by: Jon Slason

## Slide 38: Step 1: Define Households
Description
  Generate Synthetic Population using VESimHouseholds package or by loading PopulationSim outputs
Inputs
  VESimHouseholds:
    Census PUMS data provide marginal attributes
    Model-wide population control totals constrain results
  VEPopulationSim:
    PopulationSim outputs. Pre-run model that is used in the VE model inputs.
Outputs
  Household size & type (single family, multi-family, group quarters)
  Household demographics (income, etc.)
How is it used?
  Households with attributes are the basis of trip-making but also highly sensitive to cost & other policies
Presented by: Jon Slason

## Slide 39: VE Concept #1: Household Synthesis & Land Use
AZone
Population by age (Regular & GQ)
Bzone
Dwelling Units by Location Type
Employment
HH attributes
. Age mix
. Lifecycle
. Income
. Workers
. Drivers
. # Autos
BZone attributes
Urban Mixed Use
Built Form:
Density, Design, Diversity, Destination Accessibility
Employment (#, type)
LEGEND
Inputs
Model
BZone Policies
Travel Dmd Mgmt
- TDM (work)
- IMP (home)
Car Service (Hi/Lo)
Parking
- Res Pkg spaces
- Worker Pkg Pgms
- Non-Work parking
- Parking Rates
Non-Work Trips
Gravity Model
Work Location
Gravity Model
Auto Ownership model
Licensure Rate
Worker Rate
Census PUMS
Income model
AZone Per Capita Income
Household Attributes
Place Type = function of Location Type, Area Type and 4Ds
Presented by: Jon Slason
Notes: Note – Pooled Fund created a new VEPopulationSim package

## Slide 40: EPA Smart Location Database
https://www.epa.gov/smartgrowth/smart-location-mapping
EPA first released the Smart Location Database in 2011 and released version 2.0 in July 2013, and version 3.0 in 2021.
  The Smart Location Database Technical Documentation and User Guide
Interactive Map Viewer: https://epa.maps.arcgis.com/home/webmap/viewer.html?webmap=137d4e512249480c980e00807562da10
Data: https://edg.epa.gov/EPADataCommons/public/OA/SLD/SmartLocationDatabaseV3.zip
Map Server: https://geodata.epa.gov/arcgis/rest/services/OA/SmartLocationDatabase/MapServer
Key Variables
D1B
D4C
D3bpo4
D5
Presented by: Jon Slason
Notes: Note – Pooled Fund created a new VEPopulationSim package

## Slide 41: Step 2: Assign Land Use & Other Policies
Description
  Assign land use and other policies by calculating land use attributes
Inputs
  Local land use and zoning info or land use type controls
  Population, employment, and dwelling units
Outputs
  Land use density
  Land use diversity
How is it used?
  Much like ABMs, land use measures increase sensitivity to non-motorized trip-making
Presented by: Jon Slason

## Slide 42: Step 3: Assign Transportation System
Description
  Establish network information at the metropolitan area level
Inputs
  Annual revenue miles by transit type
  Peak period transit service frequency
  Highway and arterial lane miles
Outputs
  Ratio of highway & arterial lane miles to population (auto supply)
  Total daily revenue miles traveled by transit type (supply)
How is it used?
  Used as supply side; for Transit, think of this like skimming the transit network to establish supply characteristics
  Demand equations use per capita supply of lane miles and transit to estimate demand for travel.
Presented by: Jon Slason

## Slide 43: Step 4: Assign Vehicle Characteristics
Description
  Establish vehicle characteristics at the household level using logit models
Inputs
  Synthetic population (HH size, income, etc.)
  Estimated logit parameters for choice models
  Shared vehicle propensity model (changes demand for privately owned vehicle vs shared vehicles)
Outputs
  Number and age of drivers in the household
  Number and characteristics of vehicles in household
How is it used?
  This is a combination of choice models like vehicle choice
  Later used in demand calculations
  Useful in determining fleet turnover (think electrification)
Presented by: Jon Slason

## Slide 44
Vehicle Group | Vehicle Types
Household Vehicles | automobile, SUV/light truck
Car Service VMT | automobile, SUV/light truck
Commercial Service VMT | automobile, light truck
Heavy Truck VMT | heavy truck
Public Transit VMT | van, bus, rail
Vehicles, Fuels & Emissions
Presented by: Jon Slason

## Slide 45: Driverless Vehicles
Presented by: Jon Slason
The DL packages are associated with a range of updates that were made to account for Driverless Vehicles.
The packages that RSG created include several updates
“Level 3” highly connected vehicles driven by humans. Cooperative Cruise Control, etc.
“Level 5” fully automated vehicles.
New household models:
propensity for sharing (reducing owned vehicles)
propensity for L5 vehicle ownership
Features include:
deadheading
shared vs unshared price differential on car sharing
changes in roadway capacity associated with different driving characteristics (both negative and positive on capacity)
changes in travel consumed by households (parking avoidance, utility cost of driving)
VEHouseholdVehiclesDL
VELandUseDL
VESimLandUseDL
VETravelPerformanceDL

## Slide 46: HH Vehicle Attribute Models Light Truck & Vehicle Age relationships (NHTS2001)
Vehicle Age is a function of Income (table) Light Truck is a function of Income & Density (table) light truck/auto, mean veh age workers-to-drivers, dwelling type, kids, Azone ave, etc.
Presented by: Jon Slason

## Slide 47: Fuel Mix-Carbon Intensity
DETAILED FUEL MIX OPTION
Base Fuels Blends
* Fuel CI set Region-wide, except Transit optionally by MArea
COMPOSITE CI INPUTS OPTION
Electric Carbon
Intensity (by AZone)
For each Vehicle Group, scenario year:
a) Default (use with caution)
b) Detailed: Base & Blend fuel shares & Fuel Carbon Intensity by type
c) Composite Carbon Intensity
Presented by: Jon Slason

## Slide 48: Step 5: Estimate VMT
Description
  Estimate travel demand using a set of linear regression logit models
Inputs
  Supply (highway, arterial, transit)
  Synthetic population (demographics)
  Land use attributes & vehicle ownership
Outputs
  Daily Vehicle Miles of Travel and Trip Lengths
  Walk, Bike, Ride-hailing and Transit Trips
  Person miles (using Multimodal version)
How is it used?
  Much of this is core model output
Presented by: Jon Slason

## Slide 49: Household Travel
Calculate Household VMT*
(Owned & Car Service vehicles)
Estimate Household Vehicle Trips
Short Trip SOV Diversion
(trips < 20 mi round trip)
LEGEND
Inputs
Model
Household attributes
. Income
. Age mix (esp kids)
. Drivers
. Workers
. # Vehicles owned
. Parking Fees/Cash-out
...
BZone attributes
. Built Form:
Density, Design, Diversity,
Destinations Accessibility
Distance to Transit
. Urban Mixed Use
. Car Service Level
...
Transit “D”
PM peak transit stop visits within ¼ mile (Marea only)
SOV Diversion Model
. Identify HH SOV trips
by distance
. Which HHs divert trips
Overall
HH
VMT
* Budgets may affect owned vs. Car Service miles
Pricing (Cash-out worker parking, PAYD insurance) and (Car Service
reduction in) auto ownership costs may affect income
Travel Dmd Mgmt
(Home & Work based)
Alternative Mode -- Miles & Trips
Transit
Bike/short trips (<20 miles round trip)
Walk
2001 NHTS
Transport Supply (Marea only)
Road lane-miles (Arterial & Fwy)
Transit Service miles (8 modes)
Bus-Equivalent Miles per Capita
Roadway Miles
Per Capita
The default assumption is that that ECO programs reduce the average commute DVMT of participating households by 5.4%. Users can modify this value but it requires rebuilding the VELandUse package for VERSPM or VESimLandUse for VE-State.
Biking trips are defined by the proportion of short-trip SOV diversion (20 miles or less round-trip).
MultiModal Module
Presented by: Jon Slason
Notes: Order of operations;
(1) CalculateHouseholdDvmt with adj (cashout-income change, payd--why matter?, carSvc-Auto ownership change)
Budget:(2) CalculateVehicleOperatingCost
Budget:(3) Adjust it to fit within BudgetHouseholdDvmt
(4) ApplyDvmtReductions due to TDM/IIMP and Short Trips SOV Diversion.
(5) CalculateVehicleTrips and
(6) CalculateAltModeTrips.

## Slide 50: Vehicle Demand: VETravelDemand MM (VETravelDemand MM)
Original MM – Developed by Liming Wang PSU
Research: A paper on the VETravelDemandMM models structure can be found [here] (https://www.dropbox.com/s/y594fz44achoqkq/jtlu_rspm.pdf?dl=0). Here is a summary of existing and selected model structures: A broader detail-oriented on all the models alongside performance and sensitivity test can be found [here] (https://www.oregon.gov/ODOT/Programs/ResearchDocuments/SPR788RSPMTool.pdf)
MULTI-MODAL MODULE MODEL ESTIMATION SUMMARY
Original MM Multimodal Module was estimated by PSU on the 2009 NHTS.
Defined the explanatory Variables.
The Module was re-estimated by RSG (Colin Smith) using the 2017 NHTS data. The SLD and confidential NHTS data.
https://rsginc.github.io/ODOT_VEState/Model_Estimation_Summary.html
Presented by: Jon Slason
Notes: Order of operations;
(1) CalculateHouseholdDvmt with adj (cashout-income change, payd--why matter?, carSvc-Auto ownership change)
Budget:(2) CalculateVehicleOperatingCost
Budget:(3) Adjust it to fit within BudgetHouseholdDvmt
(4) ApplyDvmtReductions due to TDM/IIMP and Short Trips SOV Diversion.
(5) CalculateVehicleTrips and
(6) CalculateAltModeTrips.

## Slide 51: Alternative Modes: Travel Demand (VETravelDemand MM)
Original MM – Developed by Liming Wang PSU
Research: A paper on the VETravelDemandMM models structure can be found [here] (https://www.dropbox.com/s/y594fz44achoqkq/jtlu_rspm.pdf?dl=0). Here is a summary of existing and selected model structures: A broader detail-oriented on all the models alongside performance and sensitivity test can be found [here] (https://www.oregon.gov/ODOT/Programs/ResearchDocuments/SPR788RSPMTool.pdf)
MULTI-MODAL MODULE MODEL ESTIMATION SUMMARY ALT MODES
Original MM Multimodal Module was estimated by PSU on the 2009 NHTS.
Defined the explanatory Variables.
The Module was re-estimated by RSG (Colin Smith) using the 2017 NHTS data. The SLD and confidential NHTS data.
VarName | NHTS2009 | NHTS2017 | Ratio
(Intercept) | 0.062 | 0.264 | 4.252
AADVMT | -0.002 | -0.003 | 1.819
Age0to14 | 0.088 | 0.193 | 2.193
D1B | 0.000 | 0.001 | 1.879
D4c | 0.001 | 0.000 | -0.109
HhSize | 0.140 | 0.135 | 0.965
LifeCycleCouple w/o children | 0.000 | 0.254 | Inf
LifeCycleEmpty Nester | 0.040 | 0.159 | 4.030
LifeCycleParents w/ children | 0.072 | 0.000 | 0.000
LifeCycleSingle | -0.227 | 0.011 | -0.048
TranRevMiPC | 5.342 | 4.725 | 0.884
Table 62: Transit Trips Hurdle Model for Metro Areas, Count Model, Comparison of Models Estimated Using 2009 and 2017 NHTS Data
https://rsginc.github.io/ODOT_VEState/Model_Estimation_Summary_alt.html
Presented by: Jon Slason
Notes: Order of operations;
(1) CalculateHouseholdDvmt with adj (cashout-income change, payd--why matter?, carSvc-Auto ownership change)
Budget:(2) CalculateVehicleOperatingCost
Budget:(3) Adjust it to fit within BudgetHouseholdDvmt
(4) ApplyDvmtReductions due to TDM/IIMP and Short Trips SOV Diversion.
(5) CalculateVehicleTrips and
(6) CalculateAltModeTrips.

## Slide 52: Teleworking Alternative: (VETravelDemandWFH)
52
Teleworking – peak rates (~late 2020)
Teleworking (pre-COVID 19) by Occupation
Presented by: Jon Slason
Notes: 2019 rMove Ohio survey. Employer survey and household survey in Massachusetts were conducted.

## Slide 53: Step 6: Teleworking Alternative: (VETravelDemandWFH)
Survey data (rMove from RSG travel surveys*) was used to inform three teleworking models for the WFH Travel Demand model
Do you work outside of the home?
Yes
Do you telecommute at all?
Yes
How many days teleworking?
Model 1: Binary logit, 6.1% of workers work from home (n = 9,535 cases)
Model 2: Binary logit, if the person doesn’t work from home, do they telecommute at all during the week? (0 vs 1+) 16.6% telework at least once (n = 8,950 cases)
Model 3: Ordered logit, for those who telework, how many days?
*Ohio rMove data was able to provide detailed travel for those teleworking and those just working from home
53
Presented by: Jon Slason
Notes: 2019 rMove Ohio survey. Employer survey and household survey in Massachusetts were conducted.

## Slide 54: Teleworking Alternative: (VETravelDemandWFH)
Presented by: Jon Slason
Each telework model relies on several variables, two key variables had to be added to the VisionEval code for the WFH Travel Demand model:
  Occupation type (onsite, mixed, remote)
  Commute distance
Model 1
(Work from Home)
Worker age
Household income group
Model 2
(Teleworking)
Worker age
Model 3
(Days teleworking)
Worker age
Occupation type
Density variables for residence Census block group from SLD data
Household life cycle
Household income group
Household life cycle
Occupation type
Commute distance
Household income group
Household life cycle
Occupation type
Density variables for residence Census block group from SLD data
Commute distance
RSPM this is included. VE-State needs additional data in the package estimation
~7% WFH in 2022 & 2046

## Slide 55
Vehicle Group | Vehicle Types | Powertrain Options | Input Vehicle Adjustments | Inputs on Fuel Options
Household Vehicles | automobile, SUV/light truck | ICE, HEV, EV, PHEV | (veh sales mix) age,%LtTrk | gas/ethanol, diesel/biodiesel, CNG/RNG
Car Service VMT | automobile, SUV/light truck | ICE, HEV, EV | veh mix, age (%LtTrk same as HH) | gas/ethanol, diesel/biodiesel, CNG/RNG
Commercial Service VMT | automobile, light truck | ICE, HEV, EV | veh mix, age, %LtTrk | gas/ethanol, diesel/biodiesel, CNG/RNG
Heavy Truck VMT | heavy truck | ICE, HEV, EV | veh mix | gas/ethanol, diesel/biodiesel, LNG/RNG
Public Transit VMT | van, bus, rail | ICE, HEV, EV | veh mix | gas/ethanol, diesel/biodiesel, CNG/RNG
Vehicles, Fuels & Emissions
Presented by: Jon Slason

## Slide 56: Household Vehicles
Vehicle Table: For each HH driving age person...
On-Road Mix of Vehicles (mix of ages)
* EV may switch to PHEV if range/charging limited
Concept #4: Congestion may affect MPG
Concept #5: Budgets may affect auto ownership
HHID | Veh# | Veh Attributes | Lookup
 |  | Own-or-CarService, Age, LtTrk-or-Auto | 
HHID | Veh# | Veh Attributes* | Lookup*
 |  | Own-or-CarService, Age, LtTrk-or-Auto | Powertrain, MPG, range,...
HH attributes
. Income
. Person Age mix
. #Vehicles owned
...
BZone attributes
Car Service Availability
Urban Mixed Use
Average %LtTrk & Age
by Azone
For non-HH Vehicles
simpler approach
(on-road VMT not sales vehicles + inputs on powertrain mix, veh age, vehicle type)
2001 NHTS
Veh age & LtTrk models
Residential EV charging by DU type (SF, MF, GQ) , AZone
Daily Trip Length model
Separate tables for Autos & Light Trucks
ICE HEV PHEV EV
Presented by: Jon Slason
Notes: This module assigns drivers by age group to each household as a function of the numbers of persons and workers by age group, the household income, land use characteristics, and public transit availability. Users may specify the relative driver licensing rate relative to the model estimation data year in order to account for observed or projected changes in licensing rates.
Vehicle Range compared to 95th percentile VMT

## Slide 57: Step 7: Iterate to Balance VMT with Costs
Description
  Vehicle Miles of Travel iteratively calculated to balance with household cost
Inputs
  Initial Daily Vehicle Miles of Travel
  Network and household characteristics
  Pricing Policies
Outputs
  Converged VMT
  Household costs and Supply-side costs
How is it used?
  A bit like a network assignment this iterates to a converged solution; but this also takes household cost into account
Presented by: Jon Slason

## Slide 58: Adjust for Congestion
Sum VMT for all Vehicle Groups on the Road:
(urbanized portion of the Metropolitan Area)
Household & Car Service vehicles
Transit Vehicles
Local Delivery Commercial Vehicles
Long Haul Heavy Trucks
Allocate among Road Classes
Apply Fuel Efficiency Changes to Vehicles:
(fuel-speed curves vary by powertrain)
. due to congested speeds
. due to Speed-Smoothing policies
Adjust
Initial Conditions
Freeway
Lane-Miles
Freeway
ITS-Ops
Programs
Arterial
Lane-Miles
Arterial
ITS-Ops
Programs
Split DVMT
LEGEND
Inputs
Model
Initial “Split DVMT”
HH VMT
HH Vehicle Table
ITS-Speed Smoothing &
Eco-driving policies
2009 TTI Urban Mobility Dataset
Baseyear VMT Growth Basis
}
Calculate Speeds by Road Class
Adjust road capacity for ITS-Ops Policies
Allow re-allocation to balance speeds+Cong Fees (HH LDV only)
Balance
ITS-Ops Programs
Congestion Fees
($/mi by Road Class & Cong Level)
Presented by: Jon Slason

## Slide 59: Adjust for HH Costs & Budgets
Auto Operating Cost Adjustment
-- Limit VMT to fit HH’s Transport budget --
Auto Ownership Cost Adjustment
-- Substitute CarService for Owned Vehicles --
LEGEND
Inputs
Model
Vehicle Cost model
Auto Ownership Costs
Auto OperatingCosts
2011 ODOT Social Costs White Paper
2011 ODOT Road Cost Estimates
(Optional) Calc VMT fee to fully recover
HH share of Road Costs
VMT-based
Social Costs (or just Carbon)
* Indicates fee varies by year. Social costs & Roadway costs can vary but defaults do not.
** Estimated as Time (hrs) multiplied by value of time ($/hr) input.
Presented by: Jon Slason

## Slide 60: Adjust Auto Ownership for Car Service
HH Vehicle Table
LEGEND
Inputs
Model
2001 NHTS data
(illustrative only,
not used in VisionEval)
Since each additional vehicle has less marginal value to the household (lower VMT/person, as shown in chart below),
Could the HH save money by substituting CarService for owned autos?
Adjust HH autos owned given Car Service option
Compare vehicle ownership cost to Car Service($/mile).
(“High” Level CarService only, subject to input limitations on substitutability by vehicle type)
Presented by: Jon Slason
Notes: New model adjusts vehicle ownership by comparing the cost of owning each household vehicle per mile of travel with the cost of using car-services where the car-service level is 'High'. The cost of car-services is a user input. The user also inputs values for the assumed likelihood that a household would substitute car service use for a household vehicle where the cost is lower (separate values are specified for autos and light trucks).
Modeling Shared Vehicle Use and Automated Vehicle Ownership
The overall approach to determining which households use car services is to compare the marginal per-mile ownership of each vehicle the household owns with the per-mile cost of using a car service for an equivalent value car. For each household, the increase in VMT with each added car owned is calculated. This is divided into the cost of owning a car to calculate the marginal per-mile ownership cost. This cost for each vehicle is compared with the equivalent per-mile cost of using a car service. The household retains vehicles that have lower marginal ownership costs and eliminates vehicles that have higher marginal costs. Typically when a household gets the first vehicle, their VMT increases much more than when they add subsequent vehicles to their household fleet.
This marginal cost approach is more valid than an average cost approach because households make choices at the margin (to own one more car or one less car), and because vehicle travel and vehicle ownership costs don't scale uniformly. For example, doubling the number of cars owned does not double the miles driven. This can be seen in Table 1 which shows how the average daily vehicle miles per driving age person varies with the number of driving age persons in the household and number of household vehicles. The values are tabulated from a metropolitan area household dataset derived from the 2001 National Household Travel Survey. It can be seen that in most cases the additional miles driven per person increase at a declining rate as the number of household vehicles increases from zero to the same number of vehicles as driving age persons. For example, in the case of 2-driver households, going from one vehicle to two increases miles per driver from 16.2 to 30.2, not to 32.4. In the case of 3-driver households, going from one vehicle to three increases miles per driver from 13.3 to 29.8, not to 39.9. Consequently, the cost per mile traveled of owning an additional car increases as the number of cars owned increases.

## Slide 61: Adjust VMT for Household budget limit
Enables response to pricing policies and energy costs that increase vehicle operating costs.
Given observations that high vehicle operating costs curtail VMT,
Apply historic transportation budget portion of household income
(see chart per )
as a limit on annual vehicle operating costs.
LEGEND
Inputs
Model
HH VMT
(& Alt Mode Travel)
Transport Budget Share by Income
30% for low incomes
down to
7-10% for high
incomes
Adjust VMT for HH Budget Limit
Calculate for each household:
COSTS = Annual Vehicle Operating costs
(out-of-pocket & time-equivalent costs)
Annual HH VMT * Vehicle Operating Costs
BUDGET = Max share of Annual HH income
Transport Budget share * Annual HH Income
Reduce VMT, as needed so
COSTS stay within BUDGET.
Consumer Expenditure Survey 2003-2015
Presented by: Jon Slason
Notes: Additionally, in order to respond to pricing policies and energy costs, VisionEval imposes a budget limitation. Household VMT is constrained such that annual vehicle operating costs must stay below a maximum share of annual household income, or budget limit. A household-specific average annual vehicle operating costs is first calculated, including out-of-pocket per mile costs for each household owned and Car Service vehicles used by the household, as well as time-equivalent cost (input access times, estimates of VMT at congested speeds, and value-of-time input). Vehicle operating costs determine the proportional split of VMT among household vehicles. Out-of-pocket costs include the energy, [Maintnance, Rxxx, Tires], road use taxes (including EV surcharge and optional calculation of fee to fully recover road costs), work/non-work parking, PAYD insurance, input share of carbon and other social costs, as well as CarService fees by the household.

## Slide 62: Resume at 11am See you soon!
Presented by: Jon Slason

## Slide 63: Part 2
11:00 am – 12:30 pm
1. Overview of provided models
2. Model folder structure
3. How to run a base model
4. How to test a future scenario
Presented by: Nick Fisher
63

## Slide 64: 1. Overview of Provided Models
SJV Reference Model
SJV Reference Model with PopulationSim
SJV Scenarios Cat (Categorical) Model
Uses a custom version of VESimHouseholds to generate households and population
Generates reference Base and Future Scenarios
Used to check Base and Future model outputs
Uses PopulationSim to generate households and population
Generates reference Base and Future Scenarios
Used to check Base and Future model outputs
Uses PopulationSim
Used to create all 109 Future Scenarios
Output allows comparing of future scenarios
Output allows to goal-seek
Used in this Analysis
Provided but not being Used
Presented by: Nick Fisher

## Slide 65: Installer Structure
RSG provided the following zip file which contains the following folders:
  models: contains all 3 models
  ve-lib: contains all the R and VE packages needed to run the models. If custom packages are updated, they must be installed here (see slide 103)
    Before trying to run any models – open the VisionEval R project and run the command install.packages(“sn”)
models folder
ve-lib folder
Zip folder
Presented by: Nick Fisher

## Slide 66: 2. Model Folder Structure
Presented by: Nick Fisher

## Slide 67: Folder Structure
VisionEval models have the following folders and files:
defs:
  Directory contains the following model definition files:
  geo.csv is required at setup to be custom to the particular model. However, once built these files are infrequently manipulated.
  deflators.csv defines the annual deflator values, such as consumer price index, that are used to convert currency values between different years for currency denomination. This file does not need to be modified unless the years for which the dollar values used in the dataset is not contains in this file
  units.csv defines the units to be used for storing complex data types in the model. This files should NOT be modified.
Presented by: Nick Fisher

## Slide 68: Folder Structure
inputs:
  Directory contains all the inputs for running VE models
  Most of these files are CSV’s with one .json (model_parameters.json for Value of Time)
  See slides 20-22 for more information about inputs
  Note: “azone_ave_veh_per_hh.csv” and “reigion_hh_driver_adjust_prop.csv” are optional legacy files that do not need to be included in a customized model but are present if you install a default VE base model. Recommend deleting these files if building a custom model.
Presented by: Nick Fisher

## Slide 69: Folder Structure
results:
  Folder gets created when results are saved after a model run (see slide 73)
  Results can be saved as a CSV or SQLite database
  Also the location of log and model state files
scripts:
  run_model.R specifies the modules (steps) to be run and the packages from which they come from.
  It defines the sequence of VE modules that the model will run to generate its outputs
  All packages listed in this file must exist in the ve-lib folder
Presented by: Nick Fisher

## Slide 70: Folder Structure
visioneval.cnf:
  Defines the model’s structure and key attributes of the model and its computation stages and scenarios
  BaseYear: must match base year in input files
  Years: must match base and future year(s) in input files
queries
  Contains .VEqry files to run query output data (see slide 75-83)
    More information later in the training.
visioneval.cnf:
Presented by: Nick Fisher

## Slide 71: 3. How to run a base model
Presented by: Edna Aguilar

## Slide 72: Prerequisites
The following are needed to run a model:
SJV Base Model:
  RSG has provided an installer with the SJV base model with PopulationSim
R:
  The R version must match the R version of the installer, e.g 4.3.3
R IDE:
  RStudio: https://posit.co/download/rstudio-desktop/
Presented by: Edna Aguilar

## Slide 73: Install a VE Model
To practice how to run a model we are going to use a pre-installed model for Rogue Valley, OR.
To install the model:
Step 1: Open the R project in the root folder
Step 2: Install a default model by using the command installModel(“VERSPM”, “base”). Note: you can use the showModelIndex() function to view a list of ready-to-install models
Step 3: Confirm the model was installed in the models folder
1
2
3
Presented by: Edna Aguilar

## Slide 74: Run a VE Model
Step 1: Open the VisionEval R project in the root folder
Step 2: Open a model and save it as an object. The name of the model must match the name of the folder:
Step 3: Enter model$run() and ensure the model initializes. VisionEval uses this process to validate that the inputs are all in the anticipated format and there are no missing values across the various geographic levels.
Note: To re-run a model the ModelState.Rda file in the results folder must be deleted.
Presented by: Edna Aguilar

## Slide 75: Run a VE Model
Step 4: Extract model results
Once the model has finished running, use the built-in VE export function to export the model data as CSV outputs using the following code:
This will export the results as CSV files to the results/output folder. Depending on the number of years in the model, this process could take 15-20 minutes.
Results can also be exported into an SQLite database by using the following command. Results will also be saved in results/output.
> results$export(“sql”)
List of output tables (csv files)
Presented by: Edna Aguilar

## Slide 76: Model Outputs
Presented by: Edna Aguilar
Household table
Marea 25 table
Refer to the Metadata for variable descriptions:

## Slide 77: 4. How to test a future scenario
Presented by: Edna Aguilar

## Slide 78: DIY: Test future scenarios
Imagine you want to test different policies to reduce dvmt. Test policy changes separately and/or combined.
Step 1: Create a new model with a modified future scenario. Depending on the changes you want to implement you can install a new base model or copy another model and renaming the folder.
Step 2: Update relevant inputs to reflect the change in the future scenarios, for example:
2.1 Open the marea_congestion_charges.csv to increase congestion charge for 2038 in the high-congestion-charge and combined model
2.2 Open the azone_veh_use_taxes.csv to add vmt taxes for 2038 in the high-taxes and combined model
Presented by: Edna Aguilar
marea_congestion_charges.csv
azone_veh_use_taxes.csv

## Slide 79: DIY: Test future scenarios
Imagine you want to test different policies to reduce dvmt. Test separately or combined.
Step 3: Run all the models
Step 4: Extract results (explained in Part 3) and compare dvmt:
Scenario | DVMT
Base model | 4,980,908
High congestion charge | 4,873,635
High VMT tax | 2,668,548
High congestion charge + VMT tax (combined) | 2,606,251
Presented by: Edna Aguilar

## Slide 80: Part 3
1:00pm – 3:00pm
1. Querying outputs
2. Visualize Inputs/Outputs
3. How to run multiple future scenarios
4. Multiscenario viewer
Presented by: Edna Aguilar

## Slide 81: 1. Querying Outputs
Presented by: Edna Aguilar

## Slide 82: Background
VisionEval has a built-in query function that allows you to query the sql outputs
(To export model outputs into a sql format follow instructions in slide 73)
To query output data, a .VEqry file must be created. This file specifies the parameters of the query and follows a particular format
The “Full-Query.Veqry” file found in the queries folder explains how to specify a query and provides examples
Presented by: Edna Aguilar

## Slide 83: Anatomy of a Query
A query object is comprised of a list of queries
Each individual query is a list with the following elements:
  Name: name of measure
  Summarize or Function
    If using Function, define a string containing an R expression
    If using summarize, must define:
      Expr (required): the summarize variable expression
      Units (required): for each variable referred to in Expr or By, the units of the corresponding dataset
      By: A vector of variables along which to break out a Measure
      Table: A vector of one or more tables that will be joined
      Breaks (optional): used to turn numeric variables into categories
      BreakNames (optional): Nice names to append to the Breaks
      Key (optional): (if Table contains more than one Table) – the Dataset or field in all listed Tables to join by
  Units: The output units in which the measure is expressed
  Description: description of this measure
Presented by: Edna Aguilar

## Slide 84: Defining a .VEqry file
Look at the Metadata table for a list of variables that you could query.
Define the list of queries with all the required parameters. Look at Metadata for information about the units.
Save the .VEqry file in the queries folder
The query is run for all the model years
Presented by: Edna Aguilar

## Slide 85: How to Run a Query
Step 1: Create a .VEqry file with desired queries and save it in the queries folder
Step 2: Open R project if not already open
Step 3: Load model if not already loaded
Step 4: Load the query and run it using the query function
Step 5: Export results. Results are exported as an R Data File (.Rda) in the results folder.
Note that the .Rda file must be deleted to re-run the query.
1
3
4
5
Presented by: Edna Aguilar
5
Note:

## Slide 86: Query Results
Results are exported as a .Rda file that can be loaded in R using:
Three lists are created with each query run:
  BaseYear
  Specifications
  Values
Values contains the results of the query which can be view printing the list elements, e.g.
Presented by: Edna Aguilar
> load(file = “models/VERSPM-base/results/Query_Dvmt-Query.Rda”)

## Slide 87: Example query
Returning to the Part 2 example where we tested policies to reduce dvmt...
Run query on all models and compare results
Example query:
Presented by: Edna Aguilar

## Slide 88: DIY: Test future scenarios
Demo
Scenario | 2038 DVMT
Base model | 4,980,908
High congestion charge | 4,873,635
High VMT tax | 2,668,548
High congestion charge + VMT tax | 2,606,251
Presented by: Edna Aguilar
Going back to the previous examples where we test measures to reduce dvmt:

## Slide 89: 2. Visualizer Guide
Presented by: Edna Aguilar

## Slide 90: Input/Output Visualizer
RSG provided a Visualizer tool to visualize input and outputs for base models and to view results of the multiscenario
Presented by: Edna Aguilar

## Slide 91: Inputs Viewer
Switch between tabs
Input description
Select the base year and the year to compare it to
Select the input and the variables you want to view. Filter by Marea to focus on one Marea.
Define map (classification method) and summary chart (aggregation) settings
Input viewer: depending on the type of input, the input be summarized on a map or chart. All Marea inputs are presented in a summary table + a map or chart.
Presented by: Edna Aguilar

## Slide 92: Outputs Viewer
Select the output variable to view and the geographic scale at which to summarize
Output viewer: outputs are summarized
Select the base year and the year to compare it to
Filter data based on Marea and values
When you make changes to any of the above, you must hit go to update the output viewer
Presented by: Edna Aguilar

## Slide 93: 3. How to run multiple future scenarios
Presented by: Nick Fisher

## Slide 94: SJV VE Scenarios
Category | Level | Description | 2046 Varied Inputs
Population (P) | 1 | 2023 DOF forecast, hold household sizes fixed (reference land use inputs) | VEPopulationSimInputs
 | 2 | 20% employment growth | bzone_employment.csv
 | 3 | 2023 DOF forecast, let household sizes vary (use with reference land use inputs) | VEPopulationSimInputs
 | 4 | 2023 DOF forecast, hold household sizes fixed (run with level 1 land use inputs) | VEPopulationSimInputs
 | 5 | 2023 DOF forecast, hold household sizes fixed (run with level 2 land use inputs) | VEPopulationSimInputs
 | 6 | 2023 DOF forecast, hold household sizes fixed (run with level 3 land use inputs) | VEPopulationSimInputs
Land use (L) | 1 | Housing mix and TOD: TOD and 50% increase of multifamily shares in urban areas, 20% elsewhere | bzone_dwelling_units.csv, VEPopulationSimInputs
 | 2 | Compact growth: All growth in urbanized areas | bzone_dwelling_units.csv, VEPopulationSimInputs
 | 3 | Job-housing balance: Job to housing ratio of 1 | bzone_dwelling_units.csv, VEPopulationSimInputs
Fees / Costs (F) | 1 | 50 cents per mile congestion fee during severe and extreme congestion | marea_congestion_charges.csv
 | 2 | Congestion fees and 2.5 cents per mile VMT fee | marea_congestion_charges.csv, azone_veh_use_taxes.csv
Travel Demand Management (D) | 1 | Daily parking cost of $2 in urbanized Bzones | bzone_parking.csv
Transportation Infrastructure (T) | 1 | 2x Bus and demand response transit service | marea_transit_service.csv, bzone_transit_service.csv
 | 2 | 50% increase in bike and pedestrian facilities in urban areas | azone_prop_sov_dvmt_diverted.csv
 | 3 | 50% increase in arterial lane miles (1 scenario only) | marea_lane_miles.csv
Presented by: Nick Fisher

## Slide 95: SJV VE Scenarios – Combinations Matrix
POPULATION AND LAND USE | Fees / Costs | Travel Demand Management | Transportation Infrastructure
P1 + L0 | F0 | D0 | T0
P2 + L0 | F1 | D1 | T1
P4 + L1 | F2 |  | T2
P5 + L2 |  |  | T3
P6 + L3 |  |  | 
P3 + L0 |  |  | 
Presented by: Nick Fisher
Level 0 represents the reference level inputs (no scenario variation)
The matrix shows the combinations of elements that were run to create the scenarios. It includes:
  6 Population and Land Use scenarios
  3 Fees / Costs scenarios
  2 Travel Demand Management scenarios
  3 Transportation Infrastructure scenarios
  1 unique scenario using T3
  1 reference scenario for the base year (produces only 1 scenario)
  1 reference scenario for the future (produces only 1 scenario)
Sums to:
  (6 * 3 * 2 * 3) + 1 + 1 + 1 = 111 models being run in total

## Slide 96: The VERSPM-SJV-Cat model
This model provides the capability to quickly set up and run hundreds of models that combine unique changes to specific inputs (multiscenario design)
Model scenarios are defined in terms of combinations of individual model inputs. Inputs are defined in the scenarios folder.
SJV VE scenario inputs consist of 4 folders, each for a particular category of inputs:
  D: Travel demand management
  L: Land use
  F: Fees
  T: Transportation infrastructure
  Population sim variants are stored in the “inputs” folder
Within each category (D, L, F, T), numbered subfolders (1, 2, 3…) represent different levels of change to test for that category.
The “cat” model runs all possible combinations of categories and their levels. For example, with 3 categories each containing 3 levels, 27 unique scenario combinations are produced.
Inputs not specified in a scenario folder default to the reference model values
Presented by: Nick Fisher

## Slide 97: Future Scenario Configuration files – Model root
The VERSPM-SJV-Cat model has two config files:
  visioneval.cnf (in the root model directory), and
  scenarios/visioneval.cnf
This file is used just to define the model stages
  “stage-2022” is the reference model for 2022
  “stage-2046” is the reference model for 2046
Presented by: Nick Fisher

## Slide 98: Future Scenario Configuration files – “scenarios”
The scenarios/visioneval.cnf is a configuration file that defines the scenario elements, their levels, and the combinations in which they are run.
  This file directs the model towards specific inputs for a single model run
The “Scenario Elements” define the inputs that are changing and the magnitude of change – ex. L2 represents Compact Growth inputs.
  These elements are mirrored in the scenario folder structure
The scenario categories represent the unique combinations of scenario elements that are used – Ex. PLU 3 uses scenario elements L1 and P4.
  These categories are combined to create a single unique scenario.
Presented by: Nick Fisher

## Slide 99: Running multiple future scenarios
VisionEval treats each future scenario as a unique model that is a copy of the base model with modified inputs.
When calling model$run() on VERSPM-SJV-cat, VisionEval executes scenarios sequentially. This is computationally inefficient. RSG has provided a script that splits the models into batches to run models in parallel.
The ve_scenario_cat_to_ms_converter.R script creates new model folders (containing a batch of models) than can be run in parallel. The scenario folders are pictured here
Presented by: Nick Fisher

## Slide 100: Converting the “cat” model to multiscenario
The ve_scenario_cat_to_ms_converter.R script creates multiscenario model setup that can be run using parallel processors. This script must be run in “VisionEval.Rproj”
The modelName (name of model to break up) – this is the “cat” model.
Models can be divided into batches using the code snippet below. The numbers can be adjusted to divide the models into batches (in this case, RSG used batches of 30 models).
Presented by: Nick Fisher

## Slide 101: Running multiple future scenarios
To run a batch, simply open the VisionEval R project in the “runtime” folder and run a batch by typing the name of the right model folder, for example:
> options(future.globals.maxSize = 8.0 * 1024^3)  Set the available RAM
> model = openModel(“VERSPM-SJV-ms-model-name”)  Open the model folder
> model$plan(“multisession”, workers = 12)  Set to parallel processing and the number of processors
> model$run()  Run all of the models, this will run the “stage-2022” – or the base year – then run the scenarios in parallel (12 at a time)
Presented by: Nick Fisher

## Slide 102: 4. Multiscenario viewer
Presented by: Nick Fisher

## Slide 103: Wrapping Up
Presented by: Jon Slason

## Slide 104: What Have We Covered?
Intro to VE
What is VE
VisionEval Basics
  Inputs
  Geography structure
  Packages & Modules
  VisionEval Model Framework
Setting up Model Runs
Default and basic models
How to run a base model
How to design a future scenario
Summarizing Outputs
Querying outputs
How to run multiple future scenarios
Input/output visualizer guide
Presented by: Jon Slason
Notes: Part 1:
Slides 1 – 60
165 min: 2.75 min per slide avg.

## Slide 105: Tools and Resources
Presented by: Jon Slason
Metadata descriptions
  List of inputs and outputs from VE
  Description, Location within VE model
Shapefile
  Used along with Geos file in the “Defs” folder to create a crosswalk.
  Bzones nested within Azones nested within Mareas
Metadata description

## Slide 106: Tools and Resources
Presented by: Jon Slason
Documentation: https://visioneval.github.io/docs/
Pre-Built VE Model for the SJV Region
  Version 3.1
GitHub management
  VE core model can be enhanced with package upgrades and updates
VisionEval – Extras
  Custom SJV VisionEval packages for land use, PopulationSim, Vehicles and Powertrains
  Forked from RSG-VE-Extras which is forked from VE Pooled Fund VisionEval-Extras
Contribute to GitHub resources
  https://github.com/VisionEval
  https://github.com/RSGInc/RSG_VE_Extras

## Slide 107: Outputs and Analysis
Presented by: Jon Slason
Query methods for analyzing results for specific model runs.
  Geographic specific filters,
  database produced by VE Export function allows for users to gain access to full VE results
Web-based Visualizer to host model run data
  RSG will continue to host this resource for partners to be able to share the VE inputs, outputs, etc.
  It will continue to be enhanced over time
  RSG hosting this level of visualization as a SaaS model
https://rsginc.shinyapps.io/visioneval-explorer-sjv/

## Slide 108: Where do you go from here
Presented by: Jon Slason
Opportunities for collaboration. VE Pooled Fund is restarting outside of FHWA leadership. RSG will continue to periodically send along updates, news and announcements to current and past users of VE
Agencies around the country are using VE. For long-range plans, land use analysis, scenario planning, upstream analysis of policies prior to more detailed network modeling.
Capability to continue to refine inputs and improve model results.
Expansion – using EMAT, continuing to explore new LandUse module, ITHIM, Driverless, WFH
Develop additional model variants by changing inputs or policies of interest to you.

## Slide 109
Jonathan Slason
Project Manager
jonathan.slason@rsginc.com
Nick Fisher
Deputy Project Manager
nicholas.fisher@rsginc.com

## Slide 111: Advanced Topics
Installing a Custom Package

## Slide 112: Step 1: Clone the SJV-VE-Extras repository
1.1 Use the RSG GitHub page to clone the SJV-VE-Extras repository using your Git-compatible software of choice.
SJV-VE-Extras:
  Contains all the SJV custom packages
  Link for cloning: https://github.com/RSGInc/SJV-VE-Extras.git
The SJV VE model can be customized by modifying packages. For example, the PowertrainsAndFuelsSJV package can be changed to reflect new technology or sale projections.
Modifications to packages must happen in the source code and then installed in the appropriate ve-lib folder

## Slide 113: Step 2: Modify the package
2.1 Make your adjustments to the package files where necessary

## Slide 114: Step 3: Document the package
3.1 Open the R project in the SJV-Extras folder
3.2 Set the package folder as the working directory
3.3 Install devtools + dependencies
3.4 Run the following command to document the package:
> setwd("c:/Documents/SJV-VE-Extras/VEPowertrainsAndFuelsSJV")
> install.packages(“devtools”)
> devtools::document()

## Slide 115: Step 4: Install Packages to the VE Library
4.1 In the SJV-VE-Extras R project, add the absolute path to the ve-lib folder your model uses (e.g. installer/ve-lib). Use the “.libPaths” command:
4.2 Set the working directory to the SJV-VE-Extras folder
> .libPaths(“E:/installer/ve-lib”)
4.3 Use the “install.packages” command to install the desired VE packages (the additional commands “type” and “repos” are required as pictured).
> setwd("c:/Documents/SJV-VE-Extras")
4.4 The updated package should now appear in the ve-lib folder

## Slide 116: Step 5: Update run_model.R, necessary
5.1 If necessary, update the run_model.R script of your model so that it points to the right packages and modules